## Slide 1: Name: Jannatul Nusrat ID : 19-40885-2 SECTION: E
COURSE: DIGITAL LOGIC AND CIRCUITS
Presenter:

## Slide 2: Design a Synchronous Binary Irregular Counter [With the help of Student ID]

## Slide 3
ID-19-40885-2
I have to generate a counter sequence with my ID’s middle 5 digit.
A | B | C | D | E | 1
4 | 0 | 8 | 8 | 5 | 
4 | 0 | 8 | 10 | 5 | 
But the digit 8 is twice here so I added 2 to this and made it 10
4 👉 0 👉 8 👉 10 👉 5
8+2

## Slide 4
A=4=0100
B=0=0000
C=8=1000
D=10=1010
E=5=0101
Step 1: Binary of the Decimal Sequence
A
0100
B
0000
C
1000
D
1010
E
0101

## Slide 5
STEP-2 : Identifying the number of Flip-Flop required
Flip-Flop required = 4
K0
J0
Q0
K1
J1
Q1
K2
J2
Q2
J3
Q3
K3
C
C
C
C
Here the maximum decimal value is 10. When we convert 10 in binary digit it becomes 1010 which is a 4bit output. So we’ll require 4 Flip-Flops to design our system.

## Slide 6
Q3 | Q2 | Q1 | Q0
0 | 1 | 0 | 0
0 | 0 | 0 | 0
1 | 0 | 0 | 0
1 | 0 | 1 | 0
0 | 1 | 0 | 1
Present State
Q3 | Q2 | Q1 | Q0
0 | 0 | 0 | 0
1 | 0 | 0 | 0
1 | 0 | 1 | 0
0 | 1 | 0 | 1
0 | 1 | 0 | 0
Next State
Step 3
Binary Sequence | J3 | K3 | J2 | K2 | J1 | K1 | J0 | K0
0100 | 0 | X | X | 1 | 0 | X | 0 | X
0000 | 1 | X | 0 | X | 0 | X | 0 | X
1000 | X | 0 | 0 | X | 1 | X | 0 | X
1010 | X | 1 | 1 | X | X | 1 | 1 | X
0101 | 0 | X | X | 0 | 0 | X | X | 1
Step 5
Q(Present State) | Q(Next State) | J | K
0 | 0 | 0 | X
0 | 1 | 1 | X
1 | 0 | X | 1
1 | 1 | X | 0
Output Transition | Flip flop input
Step 3
Step 4: Transition Table

## Slide 7
 | 00 | 01 | 11 | 10
00 | 0 | x | x | x
01 | 0 | x | x | x
11 | x | x | x | x
10 | 0 | x | x | 1
 | 00 | 01 | 11 | 10
00 | 0 | x | x | x
01 | 0 | 0 | x | x
11 | x | x | x | x
10 | 1 | x | x | x
 | 00 | 01 | 11 | 10
00 | 0 | x | x | x
01 | x | x | x | x
11 | x | x | x | x
10 | 0 | x | x | 1
 | 00 | 01 | 11 | 10
00 | 1 | x | x | x
01 | 0 | 0 | x | x
11 | x | x | x | x
10 | x | x | x | x
J0=Q1
J1=Q3
J2=Q1
J3=Q2’
Q3Q2
Q1Q0
Q3Q2
Q1Q0
Q1Q0
Q1Q0
Q3Q2
Q3Q2
Step-6 : Use K-Map to derive the logic requirements

## Slide 8
 | 00 | 01 | 11 | 10
00 | X | X | X | X
01 | X | 1 | X | X
11 | X | X | X | X
10 | X | X | X | X
 | 00 | 01 | 11 | 10
00 | X | X | X | X
01 | X | X | X | X
11 | X | X | X | X
10 | X | X | X | 1
 | 00 | 01 | 11 | 10
00 | X | X | X | X
01 | 1 | 0 | X | X
11 | X | X | X | X
10 | X | X | X | X
 | 00 | 01 | 11 | 10
00 | X | X | X | X
01 | X | X | X | X
11 | X | X | X | X
10 | 0 | X | X | 1
K0=1
K1=1
K2=Q0’
K3=Q1
Q3Q2
Q3Q2
Q3Q2
Q3Q2
Q1Q0
Q1Q0
Q1Q0
Q1Q0
Step-6 continued…

## Slide 9: Final Output Connections: The equations acquired from k-maps are- 1.J0 =Q1 2.K0 = 1 3.J1 =Q3 4.K1 =1 5.J2 =Q1 6.K2 =Q’0 7.J3 =Q’2 8.K3 = Q1

## Slide 10
K0
J0
Q0
K1
J1
Q1
K2
J2
Q2
J3
Q3
K3
Q’0
Q’1
Q’2
Q’3
HIGH
HIGH
CLK
C
C
C
C

## Slide 11: Thanks For Watching!