## Slide 1: Shobhan Kumar Saha ID-19-40911-2
DIGITAL LOGIC AND CIRCUITS [E]

## Slide 2: Design a Synchronous Binary Irregular Counter. With the help of Student id

## Slide 3
ID: 19-40911-2
I have to generate a counter sequence with my id’s middle 5 digit.
ABCDEA corresponds to 40911
But the digit 1 is twice there.So I have added 1 to this.
A | B | C | D | E | 1
4 | 0 | 9 | 1 | 1 | 
4 | 0 | 9 | 1 | 2 | 1+1
But the digit 1 is twice here so I added 1 to this and make it 2
4 0 9 1 2

## Slide 4
A=4=0100
B=0=0000
C=9=1001
D=1=0001
E=2=0010
Step 1: Binary of the Decimal Sequence
A
0100
B
0000
C
1001
D
0001
E
0010

## Slide 5
STEP-2 : Indentifying the number of flifflop required
flifflop required = 4
K0
J0
Q0
K1
J1
Q1
K2
J2
Q2
J3
Q3
K3
Here the maximum decimal value is 9.when we convert 9 to binary we get 1001 which is a 4 bit output.so,we will require 4 flip-flops here to design our system

## Slide 6
Q3 | Q2 | Q1 | Q0
0 | 1 | 0 | 0
0 | 0 | 0 | 0
1 | 0 | 0 | 1
0 | 0 | 0 | 1
0 | 0 | 1 | 0
Present State
Q3 | Q2 | Q1 | Q0
0 | 0 | 0 | 0
1 | 0 | 0 | 1
0 | 0 | 0 | 1
0 | 0 | 1 | 0
0 | 1 | 0 | 0
Next State
STEP 3: COUNTER TABLE
(Filling the present state and next state values)

## Slide 7: Step 4 : Creating Transition table
QN | QN+1 | J | K
0  | 0 | 0 | X
0  | 1 | 1 | X
1  | 0 | X | 1
1  | 1 | X | 0
Output Transition | Flip flop input

## Slide 8
STEP 5: Filling up the values of J0 , K0, J1, K1, J2, K2, J3, K3
Input |  |  |  |  |  |  | 
J3 | K3 | J2 | K2 | J1 | K1 | J0 | K0
0 | X | X | 1 | 0 | X | 0 | X
1 | X | 0 | X | 0 | X | 1 | X
X | 1 | 0 | X | 0 | X | X | 0
0 | X | 0 | X | 1 | X | X | 1
0 | X | 1 | X | X | 1 | 0 | X
QN | QN+1 | J | K
0 | 0 | 0 | X
0 | 1 | 1 | X
1 | 0 | X | 1
1 | 1 | X | 0

## Slide 9
Q1 Q0 Q3 Q2 | 00 | 01 | 11 | 10
00 | 1 | x | x | 0
01 | 0 | x | x | x
11 | x | x | x | x
10 | x | x | x | x
Q1 Q0 Q3 Q2 | 00 | 01 | 11 | 10
00 | 0 | 1 | X | x
01 | 0 | X | X | X
11 | x | X | X | X
10 | x | 0 | x | X
Q1 Q0 Q3 Q2 | 00 | 01 | 11 | 10
00 | 0 | 0 | x | 1
01 | x | x | x | X
11 | x | x | x | x
10 | x | 0 | x | x
Q1 Q0 Q3 Q2 | 00 | 01 | 11 | 10
00 | 1 | 0 | x | 0
01 | 0 | x | x | x
11 | x | x | x | x
10 | x | x | x | x
Jo
J1
J2
J3
STEP 6: Use karnaugh-map to derive the logic requirement

## Slide 10
Q1 Q0 Q3 Q2 | 00 | 01 | 11 | 10
00 | x | 1 | X | X
01 | X | X | x | X
11 | X | X | X | X
10 | X | 0 | X | X
Q1 Q0 Q3 Q2 | 00 | 01 | 11 | 10
00 | X | X | X | 1
01 | X | X | x | x
11 | X | X | X | X
10 | X | X | X | X
Q1 Q0 Q3 Q2 | 00 | 01 | 11 | 10
00 | X | X | X | X
01 | 1 | X | x | x
11 | X | X | X | X
10 | X | X | X | X
Q1 Q0 Q3 Q2 | 00 | 01 | 11 | 10
00 | X | X | X | X
01 | X | X | X | X
11 | X | X | X | X
10 | x | 1 | X | X
K0
K1 =1
K2 =1
K3 =1

## Slide 11
Connections:
J0 = Q1´Q2´
J1 = Q0´Q3´
J2 = Q1´
J3= Q0´ Q1´Q2´
K0 = Q3´
K1 = 1
K2 = 1
K3 = 1

## Slide 12
STEP 7: Connecting the output in diagram

## Slide 13: Thanks For Watching!